## Slide 1: Smokeping & Cacti
  intERLab at AIT Workshop
  March 11-15 – Bangkok, Thailand
  Hervey Allen

## Slide 2: What's the Difference?
There's definite overlap, but:
Smokeping: A latency measurement and packet loss tool. Uses RRDtool to maintain it's data store. No remote daemons or services required: “SmokePing is a deluxe latency measurement tool. It can measure, store and display latency, latency distribution and packet loss. SmokePing uses RRDtool to maintain a longterm data-store and to draw pretty graphs, giving up to the minute information on the state of each network connection.”

## Slide 3: What's the Difference?
Cacti: Uses RRDtool, PHP and stores data in MySQL as well as supporting SNMP and graphing with MRTG.
“Cacti is a complete frontend to RRDTool, it stores all of the necessary information to create graphs and populate them with data in a MySQL database. The frontend is completely PHP driven. Along with being able to maintain Graphs, Data Sources, and Round Robin Archives in a database, cacti handles the data gathering. There is also SNMP support for those used to creating traffic graphs with MRTG.”

## Slide 4: Installation
We'll install both products:
Installation varies between flavors of Linux and UNIX.
It's pretty easy to to install these items under Ubuntu.
You can do massive configuration of each. We'll do some to get you started!

## Slide 5: Smokeping: Some Details
Basic install is extremely easy: apt-get install smokeping
Basic config file (/etc/smokeping/config) is simple, but you can get very complex very quickly: http://oss.oetiker.ch/smokeping/doc/smokeping_examples.en.html and, other configuration options: http://oss.oetiker.ch/smokeping/doc/smokeping_config.en.html

## Slide 6: Smokeping: The Install
sudo apt-get install smokeping
sudo apt-get install echoping
su - (to become root)‏
cd /etc/smokeping
mv config config.orig Then we will grab a copy of our local Smokeping config file, install this and go over it.
scp inst@noc:/var/www/share/conf/config .
/etc/init.d/smokeping restart

## Slide 7: Smokeping: Some Details /etc/smokeing/config
Check on latency of connection (ping)‏
Check on web server uptime and performance
Latency
++ LocalMachine
menu = The NOC
title = The noc@intERLab
host = localhost

## Slide 8: Smokeping: More Details /etc/smokeing/config
Performance/Uptime
++ NOCsquid
menu = The NOC Squid
title = www-cache / HTTP for noc@intERLab
probe = EchoPingHttp
host = localhost
port = 8080
url = http://localhost/

## Slide 9: Smokeping: The Install
There are several more examples here:
http://oss.oetiker.ch/smokeping/doc/smokeping_examples.en.html
If there is time we will play with /etc/smokeping/config to customize as you want and, maybe, to use some of the example described in the file linked above.

## Slide 10: Smokeping: The Install
Once configured, then restart the service to build the directories with RRD data:
    # /etc/init.d/smokeping restart
You can find your graphs and layout at:
    http://hostname/cgi-bin/smokeping.cgi
Lets have a look at the config file...

## Slide 11: cacti

## Slide 12: cacti: The Install
Installation is a bit tricky... (as root): apt-get install mysql-server-5.0 mysqladmin --user=root –password=instPass create cacti apt-get install cacti login with admin/admin then change

## Slide 13: apt-get install mysql-server-5.0
Enter the same password we have used during the workshop
for the inst account.

## Slide 14: apt-get install cacti
You can ignore this

## Slide 15: apt-get install cacti
Please choose “Apache2” and then Ok.

## Slide 16: apt-get install cacti
Choose “Yes” at this screen.

## Slide 17: apt-get install cacti
Enter the same password you used when installing MySQL previously. This is your inst account password.

## Slide 18: apt-get install cacti
then...
Let's use the same inst password to keep things simple.

## Slide 19: cacti: Next Steps
Next open a web browser on your machine and go to the address:
  http://localhost/cacti
You will see the following screens...

## Slide 20: apt-get install cacti
Click on “Next >>”

## Slide 21: apt-get install cacti
Be sure “New Install is chosen and press
the “Next >>” button.

## Slide 22: apt-get install cacti
Hopefully your screen looks like this. If not, let your instructor know.
Press “Finish”

## Slide 23: cacti: Initial Login
Initial login with:
User Name: admin
Password: admin

## Slide 24: cacti: Change Password
Use the same inst password to keep things simple for our workshop.

## Slide 25: cacti: Finishing
As you can see the idea is to do the following:
Define the devices you wish to monitor
Define the graphs you wish to use for each device
View and organize graphs as you want
Note that cacti takes advantage of snmp settings. As possible we'll set up some cacti graphs at this time.