## Slide 1: MRTG / RRDTool
  Network Management Workshop
  intERlab at AIT
  Thailand
March 11-15, 2008

## Slide 2: MRTG…
The Multi Router Traffic Grapher (MRTG) is a tool to monitor the traffic load on network-links. MRTG generates HTML pages containing PNG images which provide an almost live visual representation of this traffic. Check http://oss.oetiker.ch/mrtg/ to see what it does.
MRTG has been the most common network traffic measurement tool for all Service Providers
MRTG uses simple SNMP queries on a regular interval to generate graphs

## Slide 3: MRTG…
External readers for MRTG graphs can create other interpretation of data.
MRTG software can be used not only to measure network traffic on interfaces, but also build graphs of anything that has an equivalent SNMP MIB - like CPU load, Disk availability, Temperature, etc...
Data sources can be anything that provides a counter or gauge value – not necessarily SNMP.
  For example, graphing round trip times
MRTG can be extended to work with RRDTool

## Slide 4: MRTG - Issues
MRTG generates each graph (what if you have hundreds of graphs!) every 5 minutes, creating a lot of overhead.
It also has very few customizable graphing options.
Disk space is always an issue.
MRTG management itself can be tedious work.

## Slide 5: Running MRTG
Get the required packages
Compile and install the packages
Make cfg files for router interfaces with cfgmaker
Create html pages from the cfg files with indexmaker
Trigger MRTG periodically from Cron or run it in daemon mode

## Slide 6
Round Robin Database for time series data storage
Command line based
From the author of MRTG
Made to be faster and more flexible
Includes CGI and Graphing tools, plus APIs
Solves the Historical Trends and Simple Interface problems
RRDtool

## Slide 7
Define Data Sources (Inputs)‏
DS:speed:COUNTER:600:U:U
DS:fuel:GAUGE:600:U:U
  DS = Data Source
  speed, fuel = “variable” names
  COUNTER, GAUGE = variable type
  600 = heart beat – UNKNOWN returned for interval if nothing received after this amount of time
  U:U = limits on minimum and maximum variable values (U means unknown and any value is permitted)‏

## Slide 8
Define Archives (Outputs)‏
RRA:AVERAGE:0.5:1:24
RRA:AVERAGE:0.5:6:10
  RRA = Round Robin Archive
  AVERAGE = consolidation function
  0.5 = up to 50% of consolidated points may be UNKNOWN
  1:24 = this RRA keeps each sample (average over one 5 minute primary sample), 24 times (which is 2 hours worth)‏
  6:10 = one RRA keeps an average over every six 5 minute primary samples (30 minutes), 10 times (which is 5 hours worth)‏
Clear as mud!
  all depends on original step size which defaults to 5 minutes

## Slide 9
RRDtool Database Format
Recent data stored once every 5 minutes for the past 2 hours (1:24)‏
Medium length data averaged to one entry per half hour for the last 5 hours (6:10)‏
Old data averaged to one entry per day for the last 365 days (288:365)‏
--step 300
(5 minute input step size)‏
RRA 1:24
RRA 6:10
RRA 288:365
RRD
File

## Slide 10: Isn't it simple ?!
rrdtool create /var/nagios/rrd/host0_load.rrd -s 600 DS:1MIN-Load:GAUGE:1200:0:100 DS:5MIN-Load:GAUGE:1200:0:100 DS:15MIN-Load:GAUGE:1200:0:100 RRA:AVERAGE:0.5:1:50400 RRA:AVERAGE:0.5:60:43800
rrdtool create /var/nagios/rrd/host0_disk_usage.rrd -s 600 DS:root:GAUGE:1200:0:U DS:home:GAUGE:1200:0:U DS:usr:GAUGE:1200:0:U DS:var:GAUGE:1200:0:U RRA:AVERAGE:0.5:1:50400 RRA:AVERAGE:0.5:60:43800
rrdtool create /var/nagios/rrd/apricot-INTL_Ping.rrd -s 300 DS:ping:GAUGE:600:0:U RRA:AVERAGE:0.5:1:50400 RRA:AVERAGE:0.5:60:43800
rrdtool create /var/nagios/rrd/host0_total.rrd -s 300 DS:IN:COUNTER:1200:0:U DS:OUT:COUNTER:600:0:U RRA:AVERAGE:0.5:1:50400 RRA:AVERAGE:0.5:60:43800

## Slide 11
Ping Latency Graph Created by APAN from RRD Database

## Slide 12: Labs

## Slide 13: MRTG
In Ubuntu / Debian
  apt-get install mrtg
  Configuration
    /etc/mrtg/<device.mrtg>
    Global directory : /var/www/mrtg/
    Run MRTG against the configuration file from cron.

## Slide 14: cfgmaker
Uses snmpwalk and creates a mrtg configuration file
/usr/bin/cfgmaker --output=/etc/mrtg/router.mrtg --global 'workdir: /var/www/mrtg' --global 'options[_]: growright,bits' apric0t08@169.223.2.1

## Slide 15: sample
#Title[leased]: a 128K leased line
#PageTop[leased]: <H1>Our 128K link to the outside world</H1>
#Target[leased]: 1:public@router.localnet
#MaxBytes[leased]: 16000

## Slide 16: Creating HTML with indexmaker
/usr/bin/indexmaker --output=/var/www/mrtg/device.html /etc/mrtg/device.mrtg If your mrtg configuration file is well commented, the html is nice and detailed.

## Slide 17: Lab instructions
Separate paper

## Slide 18: RRDTool
# apt-get install rrdtool
# apt-get install librrdp-perl
# apt-get install librrds-perl
Add in your MRTG Configuration file
  /etc/mrtg/router.mrtg
LogFormat: rrdtool
Run mrtg
Go see in /var/www/mrtg