## Slide 1: Network Operations and Network Management
  Network Management Workshop
  intERlab at AIT
  Thailand
March 11-15, 2008

## Slide 2: Overview
What is network operations and management ?
Why network management ?
The Network Operation Center
Network monitoring systems and tools
Statistics and accounting tools
Fault/problem management
Ticket systems
Configuration management & monitoring
The big picture...

## Slide 3: What is network management ?
System & Service monitoring
  Reachability, availability
Ressource measurement/monitoring
  Capacity planning, availability
Perf. monitoring (RTT, throughput)‏
Statistics & Accounting/Metering
Fault Management
  Fault detection, troubleshooting, and tracking
  Ticketing systems, helpdesk
Change management & configuration monitoring

## Slide 4: What we don't cover...
Provisioning
  (processes associated with allocation and configuration of resources)‏
Security aspects
  Basic security is proper administration and management!

## Slide 5: Why network management ?
Make sure the network is up and running. Need to monitor it.
  Deliver projected SLAs (Service Level Agreements)‏
  Depends on policy
    What does your management expect ?
    What do your users expect ?
    What do your customers expect ?
    What does the rest of the Internet expect ?
  Is 24x7 good enough ?
    There's no such thing as 100% uptime

## Slide 6: Why network management ? - 2
What does it take to deliver 99.9 % ?
  30,5 x 24 = 762 hours a month
  (762 – (762 x .999)) x 60 = 45 minutes max of downtime a month!
Need to shutdown 1 hour / week ?
  (762 - 4) / 762 x 100 = 99.4 %
  Remember to take planned maintenance into account in your calculations, and inform your users/customers if they are included/excluded in the SLA
How is availability measured ?
  In the core ? End-to-end ? From the Internet ?)‏

## Slide 7: Why network management ? - 3
Know when to upgrade
  Is your bandwidth usage too high ?
  Where is your traffic going ?
  Do you need to get a faster line, or more providers ?
  Is the equipment too old ?
Keep an audit trace of changes
  Record all changes
  Makes it easier to find cause of problems due to upgrades and configuration changes
Where to consolidate all these functions ?
  In the Network Operation Center (NOC)‏

## Slide 8: The Network Operations Center (NOC)‏
Where it all happens
  Coordination of tasks
  Status on network and services
  Fielding of network-related incidents and complaints
  Where the tools reside (”NOC server”)‏
One of the goals of this workshop...
  Build a NOC box
  It will be the most important machine on your network
  We will do this during the week, by installing, and configuring, various tools to help in network monitoring and management.

## Slide 9: Network monitoring systems and tools
Two kinds of tools
  Diagnostic tools – used to test connectivity, ascertain that a location is reachable, or a device is up – usually active tools
  Monitoring tools – tools running in the background (”daemons” or services), which collect events, but can also initiate their own probes (using diagnostic tools), and recording the output, in a scheduled fashion.

## Slide 10: Network monitoring systems and tools - 2
Active tools
  Ping – test connectivity to a host
  Traceroute – show path to a host
  MTR – combination of ping + traceroute
  SNMP collectors (polling)‏
Passive tools
  log monitoring, SNMP trap receivers
Automated tools
  SmokePing – record and graph latency to a set of hosts, using ICMP (Ping) or other protocols
  MRTG – record and graph bandwidth usage on a switch port or network link, at regular intervals

## Slide 11: Network monitoring systems and tools - 3
Network & Service Monitoring tools
  Nagios – server and service monitor
    Can monitor pretty much anything
    HTTP, SMTP, DNS, Disk space, CPU usage, ...
    Easy to write new plugins (extensions)‏
  Basic scripting skills are required to develop simple monitoring jobs – Perl, Shellscript...
  Many good Open Source tools
    Zabbix, ZenOSS, Hyperic, ...
Use them to monitor reachability and latency in your network
  Parent-child dependency mechanisms are very useful!

## Slide 12: Network monitoring systems and tools - 4
Monitor your critical Network Services
  DNS
  Radius/LDAP/SQL
  SSH to routers
How will you be notified ?
Don't forget log collection!
  Every network device (and UNIX and Windows servers as well) can report system events using syslog
  You MUST collect and monitor your logs!
  Not doing so is one of the most common mistakes when doing network monitoring

## Slide 13: Network Management Protocols
SNMP – Simple Network Management Protocol
  Industry standard, hundreds of tools exist to exploit it
  Present on any decent network equipment
    Network throughput, errors, CPU load, temperature, ...
  UNIX and Windows implement this as well
    Disk space, running processes, ...
SSH and telnet
  It's also possible to use scripting to automate monitoring of hosts and services

## Slide 14: Statistics & accounting tools
Traffic accounting
  what is your network used for, and how much
  Useful for Quality of Service, detecting abuses, and billing (metering)‏
  Dedicated protocol: NetFlow
  Identify traffic ”flows”: protocol, source, destination, bytes
  Different tools exist to process the information
    Flowtools, flowc
    NFSen
    ...

## Slide 15: Fault & problem management
Is the problem transient ?
  Overload, temporary ressource shortage
Is the problem permanent ?
  Equipment failure, link down
How do you detect an error ?
  Monitoring!
  Customer complaints
A ticket system is essential
  Open ticket to track an event (planned or failure)‏
  Define dispatch/escalation rules
    Who handles the problem ?
    Who gets it next if no one is available ?

## Slide 16: Ticketing systems
Why are they important ?
  Track all events, failures and issues
Focal point for helpdesk communication
Use it to track all communications
  Both internal and external
Events originating from the outside:
  customer complaints
Events originating from the inside:
  System outages (direct or indirect)‏
  Planned maintenance / upgrade – Remember to notify your customers!

## Slide 17: Ticketing systems - 2
Use ticket system to follow each case, including internal communication between technicians
Each case is assigned a case number
Each case goes through a similar life cycle:
  New
  Open
  ...
  Resolved
  Closed

## Slide 18: Ticketing systems - 3
Workflow: Ticket System Helpdesk Tech Eqpt ---------------------------------------------------------------- T T T T query | | | | from ---->| | | | customer |--- request --->| | | <- ack. -- | | | | | |<-- comm --> | | | | |- fix issue -> eqpt | |<- report fix -| | customer <-|<-- respond ----| | | | | | |

## Slide 19: Ticketing systems - 4
Some ticketing software systems:
  Trac
  RT
We'll be looking at using Trac later in the workshop

## Slide 20: Configuration management & monitoring
Record changes to equipment configuration, using revision control (also for configuration files)‏
Inventory management (equipment, IPs, interfaces, ...)‏
Use version control!
  As simple as: ”cp named.conf named.conf.20070827-01”
For plain configuration files:
  CVS, Subversion
  Mercurial

## Slide 21: Configuration management & monitoring - 2
Traditionnally, used for source code (programs)‏
Works well for any text-based configuration files
  Also for binary files, but less easy to see differences
For network equipment:
  RANCID (Automatic Cisco configuration retrieval and archiving, also for other equipment types)‏

## Slide 22: Big picture
How it all fits together
- Monitoring
- Data collection
- Accounting
- Capacity planning
- Availability (SLAs)‏
- Trends
- Detect problems
Fix problems
- Improvements
- Upgrades
- Change control & monitoring
- User complaints
- Requests
- NOC Tools
- Ticket system
Ticket
Ticket
Notifications
Ticket
Ticket
Ticket

## Slide 23: Questions ?
  ?