## Slide 1: IP Basics
IP/ISP Services Workshop
July, 2010
Paro, Bhutan

## Slide 2: What is the Internet?

## Slide 3: Routing
Every host on the internet needs a way to get packets to other hosts outside its local network.
This requires special hosts called routers that can move packets between networks.
Packets may pass through many routers before they reach their destinations.
Routers make forwarding decisions based on IP addresses.

## Slide 4: So what is an IPv4 address anyway?
32 bit number (4 octet number) can be represented in lots of ways:
133
27
162
125
10000101
00011011
10100010
01111101
85
1B
A2
7D

## Slide 5: More to the structure
Hierarchical Division in IP Address:
Network Part (Prefix)
describes which network
Host Part (Host Address)
describes which host on that network
Boundary can be anywhere
used to be a multiple of 8 (/8, /16/, /24), but not usual today
Network
Host
205 . 154 . 8
1
11001101 10011010 00001000 00000001
Mask

## Slide 6: Network Masks
Network Masks help define which bits are used to describe the Network Part and which for hosts
Different Representations:
  decimal dot notation: 255.255.224.0 (128+64+32 in byte 3)
  binary: 11111111 11111111 111 00000 00000000
  hexadecimal: 0xFFFFE000
  number of network bits: /19 (8 + 8 + 3)
Binary AND of 32 bit IP address with 32 bit netmask yields network part of address

## Slide 7: Sample Netmasks
137.158.128.0/17 (netmask 255.255.128.0)
32 - 17 = 15. 2^15 = 32,768 addresses.
1000 1001
1001 1110
1 000 0000
0000 0000
1111 1111
1111 1111
1 000 0000
0000 0000
1100 0110
1000 0110
0000 0000
0000 0000
1111 1111
1111 1111
0000 0000
0000 0000
1100 1101
0010 0101
1100 0001
10 00 0000
1111 1111
1111 1111
1111 1111
11 00 0000
198.134.0.0/16 (netmask 255.255.0.0)
32 - 16 = 16. 2^16 = 65,536 addresses.
205.37.193.128/26 (netmask 255.255.255.192)
32 - 26 = 6. 2^6 = 64 addresses.

## Slide 8: Special IP Addresses
All 0’s in host part: Represents Network
e.g. 193.0.0.0/24
e.g. 138.37.128.0/17
e.g. 192.168.2.128/25 (WHY ?)
All 1’s in host part: Broadcast (all hosts on net)
e.g. 137.156.255.255 (137.156.0.0/16)
e.g. 134.132.100.255 (134.132.100.0/24)
e.g. 192.168.2.127/25 (192.168.2.0/25) (WHY ?)
127.0.0.0/8: Loopback address (127.0.0.1)
0.0.0.0: Various special purposes (DHCP, etc.)

## Slide 9: Networks – super- and subnetting
/24
/25
/27
....
By adding one bit to the netmask,
we subdivide the network into two
smaller networks. This is subnetting.
i.e.: If one has a /26 network (32 – 26 =
6 => 2^6 => 64 addresses), that network
can be subdivided into two subnets, using
a /27 netmask, where the state of the last
bit will determine which network we are
addressing (32 – 27 = 5 => 2^5 => 32
addresses). This can be done recursively
(/27 => 2 x /28 or 4 x /29, etc...).
Example: 192.168.10.0/25 (.0 - .127) can
be subnetted into 192.168.10.0 / 26 and
192.168.10.64 / 26
/27
/27
/27
/27
/27
/27
/27
/26
/26
/26
/26
/25

## Slide 10: Networks – super- and subnetting
/24
/25
/25
Inversely, if two networks can be
“joined” together under the same netmask,
which encompasses both networks, then
we are supernetting.
Example:
Networks 10.254.4.0/24 and 10.254.5.0/24
can be “joined” together into one network
expressed: 10.254.4.0/23.
Note: for this to be possible, the networks
must be contiguous, i.e. it is not possible
to supernet 10.254.5.0/24 and 10.254.6.0/24
/26
/26
/26
/26

## Slide 11: Numbering Rules
Private IP address ranges (RFC 1918)
  10/8 (10.0.0.0 – 10.255.255.255)
  192.168/16 (192.168.0.0 – 192.168.255.255)
  172.16/12 (172.16.0.0 – 172.31.255.255)
Public Address space available from APNIC
Choose a small block from whatever range you have, and subnet your networks (to avoid problems with broadcasts, and implement segmentation policies – DMZ, internal, etc...)

## Slide 12: Network settings
IP address: Your host’s IP address.
Subnet mask: The netmask of your local network. What can you talk to locally?
Default gateway: The local router. How you get packets off your local network.

## Slide 13: Network settings in FreeBSD
Files
/etc/rc.conf
/etc/netstart
/etc/hosts
/etc/resolv.conf
Commands
ifconfig eth0 196.200.218.x/24
route add default 192.200.218.254
hostname ws5.ws3.conference.sanog.org

## Slide 14: The route table
All hosts (including routers) have a route table that specifies which networks it is connected to, and how to forward packets to a gateway router that can talk to other networks.
FreeBSD routing table from “netstat –anr”
Routing tables
Internet:
Destination Gateway Flags Refs Use Netif Expire
default 196.200.218.254 UGS 4 1068 bge0
127.0.0.1 link#3 UH 0 12 lo0
196.200.218.0/24 link#1 U 0 0 bge0
196.200.218.253 link#1 UHS 0 0 lo0
Internet6:
Destination Gateway Flags Netif Expire
::1 ::1 UH lo0
fe80::%lo0/64 link#3 U lo0
fe80::1%lo0 link#3 UHS lo0
ff01:3::/32 fe80::1%lo0 U lo0
ff02::%lo0/32 fe80::1%lo0 U lo0

## Slide 15: What do route table entries mean?
Destination Gateway Flags Refs Use Netif Expire
default 196.200.218.254 UGS 4 1068 bge0
127.0.0.1 link#3 UH 0 12 lo0
196.200.218.0/24 link#1 U 0 0 bge0
196.200.218.253 link#1 UHS 0 0 lo0
The destination is a network address.
The gateway is an IP address of a router that can forward packets (or 0.0.0.0, if the packet doesn't need to be forwarded).
Flags indicate various attributes for each route:
  U Up: The route is active.
  H Host: The route destination is a single host.
  G Gateway: Send anything for this destination on to this remote system, which will figure out from there where to send it.
  S Static: This route was configured manually, not automatically generated by the system.
  C Clone: Generates a new route based on this route for hosts we connect to. This type of route normally used for local networks.
  W WasCloned: Indicated a route that was auto-configured based upon a local area network (Clone) route.
  L Link: Route involves references to Ethernet hardware.
Refs is the number of active references to this route.
Use is the count of number of packets sent using this route interface
The Netif is the network interface that is connected to that network
Expire is the seconds the ARP entry is valid

## Slide 16: How the route table is used
A packet that needs to be sent has a destination IP address.
For each entry in the route table (starting with the first):
  Compute the logical AND of the destination IP and the genmask entry.
  Compare that with the destination entry.
  If those match, send the packet out the interface, and we're done.
  If not, move on to the next entry in the table.

## Slide 17: Reaching the local network
Suppose we want to send a packet to 128.223.143.42 using this route table.
Destination Gateway Genmask Flags Interface
128.223.142.0 0.0.0.0 255.255.254.0 U bge0
0.0.0.0 128.223.142.1 0.0.0.0 UG bge0
In the first entry 128.223.143.42 AND 255.255.254.0 = 128.223.142.0
This matches the destination of the first routing table entry, so send the packet out interface bge0.
That first entry is called a network route. Do you notice anything different about this routing table?

## Slide 18: Reaching other networks
Suppose we want to send a packet to 72.14.213.99 using this route table.
Destination Gateway Genmask Flags Interface
128.223.142.0 0.0.0.0 255.255.254.0 U eth0
0.0.0.0 128.223.142.1 0.0.0.0 UG eth0
72.14.213.99 AND 255.255.254.0 = 72.14.212.0
This does not match the first entry, so move on to the next entry.
72.14.213.99 AND 0.0.0.0 = 0.0.0.0
This does match the second entry, so forward the packet to 128.223.142.1 via bge0.

## Slide 19: The default route
Note that this route table entry:
Destination Gateway Genmask Flags Interface
0.0.0.0 128.223.142.1 0.0.0.0 UG eth0
matches every possible destination IP address. This is called the default route. The gateway has to be a router capable of forwarding traffic.

## Slide 20: More complex routing
Consider this route table:
Destination Gateway Genmask Flags Interface
192.168.0.0 0.0.0.0 255.255.255.0 U eth0
192.168.1.0 0.0.0.0 255.255.255.0 U eth1
192.168.2.0 0.0.0.0 255.255.254.0 U eth2
192.168.4.0 0.0.0.0 255.255.252.0 U eth3
0.0.0.0 192.168.1.1 0.0.0.0 UG eth0
This is what a router's routing table might look like. Note that there are multiple interfaces for multiple local networks, and a gateway that can reach other networks.

## Slide 21: Forwarding packets
Any UNIX-like (and other) operating system can function as gateway:
  In FreeBSD in /etc/rc.conf set: gateway_enable="YES"
Without forwarding enabled, the box will not forward packets from one interface to another: it is simply a host with multiple interfaces.