Basic radio physics
Sebastian Büttrich, NSRC/ITU/wire.less.dk
edit: September 2010
http://creativecommons.org/licenses/by-nc-sa/3.0/

---
Antenna
Electromagnetic Fields
- Electromagnetic forces act between electric charges and electric currents.
- For every point in space, an electromagnetic field (the force at that very point) can be defined and measured.
- E Electric Field, H Magnetic Field
- Electromagnetic waves are fields travelling in space

---
Electromagnetic Waves
- Examples of electromagnetic waves are: Light, Xrays, Microwaves, FM Radio waves.
- Electromagnetic waves need no medium – they are
  the dance without a dancer
  (compare: sound waves)

---
Electromagnetic Waves
- c = l * n
- c is the speed of light (3×108 m/s)
- l Lambda is the wavelength [m]
- n Nu is the frequency [1/s = Hz]
- Light needs 1.3 seconds from the moon to earth, and 8 minutes from the sun … and how long for 100 km? ...

---
A wave

---
Reminder: powers of ten
- Centi-	10-2	1/100
- Milli-	10-3	1/1000
- Kilo-	103	1,000
- Mega-	106	1,000,000
- Giga-	109	1,000,000,000

---
Electromagnetic Waves: Polarization
- Direction of the electric field vector
- Linear, elliptic, circular polarization

---
Example: Dipole

---
Electromagnetic spectrum
Examples

---
Use of electromagnetic spectrum

---
Use of electromagnetic spectrum

---
Frequencies in wireless networking
- Focus on the ISM (license exempt) bands at
  2.4 Ghz – 802.11b/g – 12 cm
  5.x Ghz – 802.11a – 5...6 cm
- Other bands:
  915 Mhz
  3.5 GHz
  and more

---
Propagation of Radio waves
- Wavefronts
- Huygens principle: at any point, spherical waves start
- Therefore, radio waves (like light) do not propagate as a straight line .. not even light does that
- Behavior scales with wavelength

---
Huygens principle

---
Radio waves
- Absorption
- Reflection
- Diffraction
- Interference

---
Radio waves: Absorption
Two main enemies :)
- Metal
- Water (rain, fog, waterpipes, …)
  discuss:
- Stones, bricks, concrete
- Wood , trees
- People: well .... we are water ....
- Power decreases exponentially in material: linear decrease in dB

---
Radio waves: Reflection
- e.g. on Metal
- angle in = angle out
  plane
  parabole

---
Radio waves: Diffraction
Diffraction is the apparent bending and spreading of waves when they meet an obstruction. Scales roughly with wavelength.

---
Radio waves: Interference
- Waves can annihilate each other, so that 1 + 1 = 0
- In wireless technology, the word Interference is typically used in a wider sense, for all kinds of disturbance through other RF sources, e.g. neighbouring channels.

---
Radio waves: Frequency dependence of behaviour
- Rule of thumb: the longer the wavelength, the further it goes
- Rule of thumb: the longer the wavelength, the better it goes through and around things
- Rule of thumb: the shorter the wavelength, the more data it can transport

---
Radio propagation in free space
- Free space loss
- Fresnel zones
- Line of Sight

---
Free Space Loss
Proportional to the square of the distance and also proportional to the square of the radio frequency
FSL [dB]= C + 20 * Log(D) + 20 * Log(F)
D distance, and F frequency [MHz].
The constant C is 36.6 if D is in miles, and 32.5 if D is in kilometers.

---
Fresnel zones

---
Line of sight
In general, you need to have a free line of sight (LOS) for a radio link

---
Example: A full transmission path
Image: radio – cable – antenna – free space – antenna – cable - radio

---
The dB
- Definition: 10 * Log (P1 / P0)
- 3 dB	= double power
  10 dB	= order of magnitude = x 10
- Calculating in dBs
- Relative dBs:
  dBm = relative to 1 mW
  dBi = relative to ideal isotropic antenna

---
The dB: Examples
- 1 mW	=	0 dBm
- 100 mW	=	20 dBm
- 1 W	=	30 dBm
- An omni antenna with 6 dBi gain
- A cable (RG213) with 0.5 dB/m loss

---
Transmit Power
Example from a 802.11a/b card:
Output Power:
802.11b: 18 dBm (65 mW) peak power 802.11a: 20 dBm (100 mW) peak power

---
Receive sensitivity
Example from a Senao 802.11b card
Receive Sensitivity:
1 Mbps:	-95 dBm;
2 Mbps:	-93 dBm;
5.5 Mbps:	-91 dBm
11 Mbps:	-89 dBm

---
Where physics matter
- Always!
  ... and especially ...
  (some real life examples based on trainer's experience)
- when an access point is placed under a desk
- when winter turns to springtime ...
- when it is rush hour in the city ...
- when doing very long distance links (speed of light!)
- when you need to tell marketing talk from truth

---
Examples: Office network
- Offices typically have massive multipath conditions
- Problem objects: People :), metal infrastructure (computers, radiators, desks, even CDs!)
- Choice of locations and antennas essential

---
Examples: when winter turns to spring ...
- Regardless of your climate zone, factors like vegetation, humidity, rain etc change with the seasons!
- Dry trees might be transparent, green trees are not!

---
Examples: when it's rush hour in the city
- In urban environments, conditions change with the hour ... people, vans, cars, electromagnetic interference, ...
- Verify on a monday what you measure on a sunday :)

---
Examples: when speed of light comes into play
- Standard implementations of 802.11_ standards set time-out windows: PCF, DIFS, SIFS, ...
- For long distance links, the travel time of the signal might lead to timeout and performance losses
- We have to hack the MAC layer to go long distance … see e.g. TIER group, Berkeley

---
Examples: looking through marketing talk, e.g. .....
- One antenna or radio device NEVER has a reach or distance ... that is one hand clapping …
- Even with WIMAX' NLOS (None line of sight), waves still do not go through absorbing walls
- Even $$$$ enterprise wireless fails, if you forget to check polarization