Multimedia Training Kit
Link budget
Sebastian Büttrich, NSRC
edit: sept 2010, GARNET

---
Elements of a radio link
- Effective transmit power: transmit power [dBm] - (cable + connector) loss [dB] + amplifier gain [dB] + antenna gain [dBi]
- Propagation loss [dB]: Free space loss [dB]
- Effective receiving sensibility: antenna gain[dBi] + amplifier gain [dB] - cable loss [dB] - receiver sensitivity [dBm]

---
The elements one by one
- Complete radio link calculation is simply a sum of all contributions, as long as all values are in dBs
- All positive values are gain
- All negative values are losses

---
Terms
- Link Budget / Power Budget / System gain
- System operating margin
- SNR: Signal-to-Noise ratio
- EIRP: Effective Isotropic Radiated Power

---
Transmit power
- what comes out of the radio unit
- depends on legal limits and thus on country/region
- check vendor's tech specifications
- typical in 802.11b:
  15 ... 20 dBm (30 ... 100 mW)

---
Transmit Power
Example from a 802.11a/b card:
Output Power:
802.11b: 18 dBm (65 mW) peak power 802.11a: 20 dBm (100 mW) peak power

---
Cable loss
- Rule: Antenna cable should be as short as possible
- Typical loss values range from
  1 dB/m down to < 0.1 dB/m
- Frequency dependent
- Check datasheets (and verify)

---
Cable loss: typical values
- Antenna Type	loss [dB/100m]
- RG 58	ca. 80-100	“thin black”
- RG213	ca. 50	“big black”
- LMR-200	50
- LMR-400	22
- Aircom plus	22
- LMR-600	14
- 1/2” Flexline	12
- 7/8”	Flexline	6.6

---
Cable loss – connectors
- Allow at least – 0.25 dB (loss) for each connector in your cabling
- Check data sheets for loss at your frequency
- Lightning arrestors (circa 1 dB)

---
Amplifiers
- optionally, amplifiers might be used
- high quality amplifiers are expensive
- amplifiers may change frequency characteristics (broadening) and add noise
- intelligently optimized antennas and high receive sensitivity are better than brute force amplification
- consider legal limits

---
Antenna – TX
- Antenna gains range:
  2 dBi (simple integrated antennas)
  5 dBi (standard omnidirectionals)
  up to
  25-30 dBi (paraboles)
- verify that you really get nominal gain
  (tilt losses, polarization losses, etc)

---
Free Space Loss
- Proportional to the square of the distance and also proportional to the square of the radio frequency
- FSL [dB]= C + 20 * Log(D) + 20 * Log(F)
  D distance, and F frequency [MHz].
  The constant C is 36.6 if D is in miles, and 32.5 if D is in kilometers.

---
Free Space Propagation: Fresnel zones
- r = 17.33 sqrt(d1*d2/f*d)	radius for first zone [m]
  d1, d2 distances from obstacle to link end points,
  d link distance [km], f [GHz]
- if d1 = d2 ( = obstacle in the middle)
  r = 17.33 sqrt (d / 4*f)
- r (60%) = 10.4. ( d / 4*f )

---
Antenna – RX
Same as Antenna – TX

---
Cable on receive side
same as on transmit side

---
Amplifiers on receive side
- same as on transmit side
- again, not a suggested method

---
Receive sensitivity
- Typical values are circa -85 dBm for maximum data rate
- Example: Orinoco cards PCMCIA Silver/Gold 11Mbps => -82 dBm ; 5.5Mbps => -87 dBm; 2Mbps=> -91 dBm; 1Mbps=> -94 dBm.
- Example: Senao 802.11b card
  11 Mbps => -89dBm; 5.5 Mbps =>-91dBm
  2 Mbps => -93dBm; 1 Mbps => -95dBm

---
Complete link budget – ex. 1
- Transmit output	+ 015 dBm
- Cable + Connectors	- 003 dB
- Antenna TX	+ 024 dBi
- FSL (50 km / 31.1 miles at 2.4 Ghz)
  - 134 dB
- Antenna RX	+ 024 dBi
- Cable + Connectors	- 003 dB
- Receive Sensitivity	- 085 dBm (subtract!)
  ------------------------------------------------------------------------
- TOTAL	+ 008 dB margin

---
Complete link budget – ex. 1

---
Complete link budget – ex. 2
- Transmit output	+ 018 dBm
- Cable + Connectors	- 005 dB (low quality cabling)
- Antenna TX	+ 005 dBi (an omni)
- FSL (1 km / 0.622 miles at 2.4 Ghz)
  - 100 dB
- Antenna RX	+ 008 dBi (patch antenna
- Cable + Connectors	- 005 dB (bad again :)
- Receive Sensitivity	- 092 dBm (subtract!)
  ------------------------------------------------------------------------
- TOTAL	+ 13 dB margin

---
Complete link budget – ex. 2