## Slide 1: perfSONAR Toolkit 3.5: What’s Coming Next?

## Slide 2: Main themes
Support for central host management and node auto-configuration
Support for low cost nodes
Support for Debian, VMs, and other installation options
Modernize the GUIs
Timeline:
  rc1 in July
  final release in September

## Slide 3: Expanded perfSONAR Use Cases
Current Use Case
  perfSONAR Toolkit
    Includes CentOS 6 and all perfSONAR components
New Use Cases
  perfSONAR tools only
    Support for both RHEL-based and Debian-based hosts
  perfSONAR hosts that are centrally managed
  perfSONAR hosts that ‘self-configure’
  NDT only host

## Slide 4: Current perfSONAR components
Measurement tools
  iperf3, bwctl, owamp, traceroute, etc.
Measurement archive
Central test mesh management tools
Host management tools
  Configure tests, configure NTP, etc.
Data analysis tools
  Plot data from the archive
  Dashboard tools
Lookup Service

## Slide 5: Improved Support for Central Management
Goals:
  Make it easy to incorporate perfSONAR hosts into existing host management systems (puppet, chef, SaltStack, cfengine, etc.)
  Make it easy to manage many perfSONAR hosts at a single institution
  New rpm and debian bundles to support this

## Slide 6: Test Node Auto-Configuration
Goal: perfSONAR node that will require zero configuration
Site will register in the lookup service:
  What hosts to run tests to
  Where to send the test results
Assumes DHCP to get node address
Primary use case is for sites with several nodes

## Slide 7: perfSONAR for Network Researchers
Active measurement interesting for network researchers
  Traceroute data automatically collected along with bwctl/owamp results
Data easy to download for analysis
  esmond-ps-get-bulk
    Output CSV or JSON
    See: https://pypi.python.org/pypi/esmond_client
Notes: New tool makes it easy to download data from perfSONAR measurement archives for analysis

## Slide 8: perfSONAR Hardware
Good 1U host able to sustain 10Gbps TCP are increasingly cheaper
  $500 (+10G NIC cost).
  See perfSONAR user list for sample configs
Cheap 1Gbps server now avaiable for $100
  Intel Celeron-based (ARM is not fast enough)
  e.g.: http://www.newegg.com/Product/Product.aspx?Item=N82E16856501007
VMs are not recommended
  Tools work better if can guarantee NIC isolation
Notes: These days you can get a good 1U host capable of pushing 10Gbps TCP for around $500 (+10G NIC cost).
  See perfSONAR user list

## Slide 9: User Interface Refresh
Easy to use web interface
Targeted at users with variety of levels of technical expertise.
Our goals in perSONAR 3.5:
improve easy of use and visual appeal
integration of state of the art UI components
to extend UI lifespan.
Current Interface

## Slide 10: New Host Management Interface

## Slide 11: Updated psUI
Notes: psUI lets you run tests on demand, and also review historical results

## Slide 12: perfSONAR UI and eduGAIN

## Slide 13: perfSONAR web user interface

## Slide 14: Dynamic discovery of sites through Lookup Service

## Slide 15: Search filter and remote check of availability

## Slide 16: Useful URLs
http://docs.perfsonar.net/
https://www.perfsonar.net/
http://fasterdata.es.net/
  http://fasterdata.es.net/performance-testing/network-troubleshooting-tools/
https://github.com/perfsonar
  https://github.com/perfsonar/project/wiki