## Slide 1: Country Report on IP/ISP Network
By
Bredalyn Jatios & Douglas Kilemente
Marshall Islands National Telecommunications Authority

## Slide 2: I.T Dept
Managing/Configuring/Installing/Monitoring/ Troubleshooting/Deploying/Maintaining:
  miNTA Backbone Network
  miNTA Internet Services
  Virtual Machines (VMWare)- Servers
  External Tech Support
  Internal Tech Support
  UniFi Hotspot

## Slide 3: miNTA’s Network
Backbone consists of 90+ switches, storage medias and routers:
  Majuro and Ebeye backbone switches (Cisco)
  Cisco routers – Border, distribution, access
  NAS/SAN- Synology/Brocade
  DSLAMs- ADSL/VDSL; Zhone and Calix
  Ubiquiti (Rockets, NanoStations, Access Points)- Hot Spots

## Slide 5: miNTA Virtual Machines: VMWare
Houses Servers for:
  miNTA’s AD, Anti-Virus, VPN, etc.
  SIP-Server
  Thin Clients
  Monitoring System:
    Cacti
    SPAM
    WhatsUpGold
    Nagios
    UniFi Controller

## Slide 6: External/Internal Tech Support
Extra Paid service
Maintain fast data flow within the network and in and out of the network
Provide NAT, IP Routing, and UDP or TCP port forwarding
Network Security and Audit.
Monitoring System (CPU, Memory, disk, and Bandwidth Usage)
----Cacti
----Whatsup Gold
----Nagios
Internal SIP services (VOIP)

## Slide 7: Internet Services
Internet- High Speed DSL, email, and Hot Spots
DAMA- Demand Assigned
Multiple Access Satellite System for
Outer Islands
Leased Line(FTTx or ADSL or VDSL)
UniFi- for Hot Spots
Air Fiber
VoIP

## Slide 8: Overall DSL Port Status

## Slide 9: DSL Port Break Down

## Slide 10: Leased Line/FTTx

## Slide 13: HOT Spots-UniFi
Available only in Majuro and Ebeye
each hotspot up to 30 mbps
23 Coverage Areas including 4 of the islets and portable Wi-Fi on fishing ships throughout the lagoon
The current total subscriber of our Wi-Fi service is 500.

## Slide 15: On-going Projects
Ubiquiti Air Fiber link between Majuro and Arno
Introducing VoIP services into Market
Dual Stacking edge routers- miNTA prepping for IPv6. Core is mostly done, now working on end
build more Hot Spots in Ebeye
Create a Data Center for hosting- miNTA to play both Registry and Registrar role?(pending Government election)
update miNTA website-include customer portal.
Setup more FTTx

## Slide 16: Challenges
Backing up Fiber connection with Guam
Provide higher bandwidth for Outer Islands
Deploy Hybrid(NAS and SAN)
Repairing main copper cable; troubleshooting Outer islands; raising employee capacity
Keeping up with the demand for higher speeds
Create more efficient Monitoring System
  SPAM/Intrusion/DoS detection and mitigation
  User protection from hackers, bots, and other harmful programs

## Slide 17: Conclusion
Questions???
Thank you!!!