## Slide 1
NfSen
Network Management &
Monitoring
Notes: 10/28/10
<number>
10/28/10
<number>

## Slide 2
Companion to NfDump tools
NfDump tools collect netflow data and store them in files
Processing netflow data with NfDump tools can only be done on the command line
NfSen is a graphical (Web Based) front end to NfDump
Creates RRD graphs based on stored data
Plugins extend the functionality of base (e.g. PortTracker and SURFmap)
What is NfSen
Notes: 10/28/10
<number>
<number>

## Slide 3
NfSen allows you to:
  Easily navigate through the netflow data
  Process the netflow data within the specified time span
  Create history as well as continuous profiles
  Set alerts, based on various conditions
  Write your own plugins to process netflow data on a regular interval
What can you do with NfSen
Notes: 10/28/10
<number>
<number>

## Slide 4
NfSen Architecture
Notes: 10/28/10
<number>
<number>

## Slide 5
NfSen: Points to note
Every 5 minutes nfcapd starts a new file, and nfsen processes the previous one
Hence each graph point covers 5 minutes
The graph shows you the total of selected traffic in that 5-minute period
To get more detailed information on the individual flows in that period, nfsen lets you drill down using nfdump in the back end

## Slide 6
NfSen structure
Configuration file - nfsen.conf
NfDump files – Netflow files containing collected flows stored in the directory: /var/nfsen/profiles-data
  Note: It is possible for other programs to read NFDump files but don’t store them for too long as they can fill up your drive
Actual graphs – stored in the directory: /var/nfsen/profiles-stat

## Slide 7
NfSen Home Screen
Notes: 10/28/10
<number>
<number>

## Slide 8
Graphs of flows, packets and traffic based on interface with NetFlow activated
Note: What is seen under Traffic should closely match what your NMS shows for the same interface
Graphs Tab
Notes: 10/28/10
<number>
<number>

## Slide 9
Most interesting page
Can view present flow information or stored flow information
Can view detailed NetFlow information such as
  AS Numbers (more useful if you have full routing table exported on your router)
  Src hosts/ports, destination hosts and ports
  Unidirectional or Bi-directional flows
  Flows on specific interfaces
  Protocols and TOS
Details Page
Notes: 10/28/10
<number>
<number>

## Slide 10
Routers being monitored
Graph of Netflow traffic for all Protocols
Time period for flows being observed
Netflow traffic graphs organized by Protocol
Extended Netflow processing options
Notes: 10/28/10
<number>
<number>

## Slide 11
A channel is a type of traffic of interest
  Total HTTP, HTTPS, SMTP traffic (etc)
  Traffic to and from the Science department
A profile is a collection of channels which can be shown together in a graph
  v4 TCP, v6 TCP, v4 UDP, v6 UDP, Other
You can create your own profiles and channels, and hence graphs.
Use filters to define a channel
  Filter out the flow data you are interested in from the data files that contain all the flows
Profiles and Channels
Notes: 10/28/10
<number>
<number>

## Slide 12
A filter is a collection of expressions
  expr1, expr2 and expr3, expr4 or expr5, not expr6, ( expr7 ), not ( expr8 )
Each expression can specify things like
  IP version: inet, ipv4, inet6, ipv6
  ProtocoI: {proto} tcp, udp, icmp, gre, …
  IP Address: [src|dst] ip 10.10.10.1 [src|dst] ip in <addr1> <addr2> <addr3>
Filters
Notes: 10/28/10
<number>
<number>

## Slide 13
IP Network: [src|dst] net 172.16/16
Port: [src|dst] port 80 [src|dst] port > 1024
TCP Flags: flags S flags S and not flags AFPRU
TOS: tos 8
Filters (ctd)
Notes: 10/28/10
<number>
<number>

## Slide 14
Bytes: bytes > 1024 bytes = 64
Packets per second: pps > 10
Bits per second: bps > 10m
Bits per packet: bpp > 15
Duration of flow: duration > 36000000
AS Number: [src|dst] 23456
All numbers can have scaling factors: k, m, g, t with 1024 as factor
Filters (ctd)
Notes: 10/28/10
<number>
<number>

## Slide 15
proto tcp and ( port 80 or port 443)
proto tcp and ( src ip 172.16.17.18 or dst ip 172.16.17.19)
proto tcp and ( net 172.16/16 and src port > 1024 and dst port 80 ) and bytes > 2048
ipv6 and proto tcp and ( port 80 or port 443)
Example filters
Notes: 10/28/10
<number>
<number>

## Slide 16
A profile is a collection of channels graphed together
Profiles and Channels
Notes: 10/28/10
<number>
<number>

## Slide 17
Alerts Page
  Can create alerts based on set thresholds eg, increase or decrease of traffic
  Emails can be sent once alarm is triggered
Stats page
  Can create graphs based on specific information
    ASNs,
    Host/Destination IPs/Ports
    In/Out interfaces
    Among others
Alerts and Stats
Notes: 10/28/10
<number>
<number>

## Slide 18
Several plugins available:
PortTracker tracks the top 10 most active ports and displays a graph
SURFmap displays country based traffic based on a Geo-Locator
More plugins available here http://sourceforge.net/projects/ nfsen-plugins/
Plugins
Notes: 10/28/10
<number>
<number>

## Slide 19
PortTracker
Notes: 10/28/10
<number>
<number>

## Slide 20
SURFMap
Notes: 10/28/10
<number>
<number>

## Slide 21
Can be used for:
  Forensic work: which hosts were active at a specific time
  Viewing src/dst AS traffic, src/dst port/IP traffic among many other options
  Identifying most active IPs or Protocols
It is a tool to complement your NMS so that you can have more detailed info regarding the traffic
With this information, you can make an informed decision eg:
  You have a high amount of SMTP traffic, some machines could be sending out spam
  80% of your traffic is to ASN X. Perhaps its wise to connect directly with that network and save costs
When to use NfSen
Notes: 10/28/10
<number>
<number>

## Slide 22
Bidirectional vs Unidirectional traffic as seen via NfSen
Notes: 10/28/10
<number>
<number>

## Slide 23
Unidirectional shows flows from host A to B and then host B to host A
Bidirectional shows flows between Host A and B combined
Can be used with any of the other filters (src port, src host plus many more)
List of filters can be found here:
  http://nfsen.sourceforge.net/#mozTocId652064
Unidirectional and Bidirectional
Notes: 10/28/10
<number>
<number>

## Slide 24
Bidirectional (Details tab)
You need to select either a Singe Timeslot or Time Window
Notes: 10/28/10
<number>
<number>

## Slide 25
Unidirectional (Details tab)
Notes: 10/28/10
<number>
<number>

## Slide 26
NfSen
  http://nfsen.sourceforge.net
NfDump
  http://nfdump.sourceforge.net/ This is a good read to better understand NfSen, NfDump and nfcapd.
References
Notes: 10/28/10
<number>
<number>

## Slide 27
Exercises